## Slide 1: Module 8
Implementing IPv6
Notes: Presentation: 60 minutes
Lab: 45 minutes
After completing this module, students should be able to:
Describe the features and benefits of Internet Protocol version 6 (IPv6).
Describe IPv6 addressing.
Describe IPv6 coexistence with Internet Protocol version 4 (IPv4).
Describe IPv6 transition technologies.
Required Materials
To teach this module, you need the Microsoft® Office PowerPoint® file 20410D_08.pptx.
Important: We recommend that you use Office PowerPoint 2007 or a newer version to display the slides for this course. If you use PowerPoint Viewer or an older version of Office PowerPoint, all the features of the slides might not display correctly.
Preparation Tasks
To prepare for this module:
Read all of the materials for this module.
Practice performing the demonstrations and the lab exercises.
Work through the Module Review and Takeaways section, and determine how you will use this section to reinforce student learning and promote knowledge transfer to on‑the‑job performance.
20410D
8: Implementing IPv6

## Slide 2: Module Overview
Overview of IPv6 IPv6 Addressing Coexistence with IPv4 IPv6 Transition Technologies
Notes: Provide a brief overview of the module contents.
20410D
8: Implementing IPv6

## Slide 3: Lesson 1: Overview of IPv6
Benefits of IPv6 Differences Between IPv4 and IPv6 IPv6 Address Format
Notes: Provide an overview of the topics that this lesson will discuss. Explain that in this lesson, you will compare IPv4 and IPv6, so that students understand the differences between the two more fully.
20410D
8: Implementing IPv6

## Slide 4: Benefits of IPv6
Benefits of IPv6 include:
Larger address space
Hierarchical addressing and routing infrastructure
Stateless and stateful address configuration
Required support for IPsec
End-to-end communication
Required support for QoS
Improved support for single-subnet environments
Extensibility
Notes: Highlight the benefits of IPv6 that are most likely to appeal to students, including:
Larger address space
Stateful and stateless configuration
End‑to‑end communication
Quality of Service (QoS)
Note that some of these benefits were implemented widely in IPv4, but were not required. For example, Internet Protocol security (IPsec) and QoS.
20410D
8: Implementing IPv6

## Slide 5: Differences Between IPv4 and IPv6
Placeholder to ensure the table gets published correctly. This should sit behind the table and not be visible.
Feature | IPv4 | IPv6
Fragmentation | Performed by routers and sending host | Performed only by sending host
Address resolution | Broadcast ARP request frames | Multicast Neighbor Solicitation messages
Manage multicast group membership | IGMP | Multicast listener discovery
Router discovery | ICMP Router Discovery (optional) | ICMPv6 Router Solicitation and Router Advertisement (required)
DNS host records | A records | AAAA records
DNS reverse lookup zones | IN-ADDR.ARPA | IP6.ARPA
Minimum packet size | 576 bytes | 1280 bytes
Notes: Use this topic to expand on the differences between IPv4 and IPv6 that the previous topic discussed. Note that this topic does not repeat information that the previous topic provided, and it is not a comprehensive list of the differences between the versions. Vary your coverage of this content based on the interest of your students and your comfort with in‑depth networking topics.
20410D
8: Implementing IPv6

## Slide 6: IPv6 Address Format
128-bit address in binary:
  00100000000000010000110110111000000000000000000000101111001110110000001010101010000000001111111111111110001010001001110001011010
128-bit address divided into 16-bit blocks:
0010000000000001 0000110110111000 0000000000000000 0010111100111011 0000001010101010 0000000011111111 1111111000101000 1001110001011010
Each 16-bit block converted to hex (base 16):
2001:0DB8:0000:2F3B:02AA:00FF:FE28:9C5A
Further simplified by removing leading zeros:
2001:DB8:0:2F3B:2AA:FF:FE28:9C5A
Notes: This slide shows the example from the text laid out in four rows. Use this slide, and the next four slides, as a five-frame build slide.
Guide students through the process of converting the binary IPv6 address on the slide to hexadecimal. It is not important that students have a strong grasp of the manual details. This topic is meant to provide students with an overview.
Consider showing a demonstration of binary to decimal to hexadecimal with the Windows Server 2012 Calculator app.
20410D
8: Implementing IPv6

## Slide 7: IPv6 Address Format
[0010][1111][0011][1011]
Notes: This is the 2nd of 5 frames.
It shows a 16‑bit binary number divided into 4 groups of 4 bits each.
20410D
8: Implementing IPv6

## Slide 8: IPv6 Address Format
8 4 2 1
[0 0 1 0]
0+0+2+0=2
[1 1 1 1]
8+4+2+1=F
[0 0 1 1]
0+0+2+1=3
[1 0 1 1]
8+0+2+1=B
[0010][1111][0011][1011]
Notes: This is the 3rd of 5 frames.
Each group of 4 bits from the previous frame is converted to a hexadecimal digit.
20410D
8: Implementing IPv6

## Slide 9: IPv6 Address Format
= 2F3B
8 4 2 1
[0 0 1 0]
0+0+2+0=2
[1 1 1 1]
8+4+2+1=F
[0 0 1 1]
0+0+2+1=3
[1 0 1 1]
8+0+2+1=B
[0010][1111][0011][1011]
Notes: This is the 4th of 5 frames.
The 4 hexadecimal digits from the previous frame are combined to make a 4‑digit hexadecimal number.
20410D
8: Implementing IPv6

## Slide 10: IPv6 Address Format
128-bit address in binary:
  00100000000000010000110110111000000000000000000000101111001110110000001010101010000000001111111111111110001010001001110001011010
128-bit address divided into 16-bit blocks:
0010000000000001 0000110110111000 0000000000000000 0010111100111011 0000001010101010 0000000011111111 1111111000101000 1001110001011010
Each 16-bit block converted to hex (base 16):
2001:0DB8:0000:2F3B:02AA:00FF:FE28:9C5A
Further simplified by removing leading zeros:
2001:DB8:0:2F3B:2AA:FF:FE28:9C5A
Notes: This is the 5th of 5 frames. It is a repeat of the first frame, and it depicts the example laid out in four rows.
20410D
8: Implementing IPv6

## Slide 11: Lesson 2: IPv6 Addressing
IPv6 Address Structure Global Unicast Addresses Unique Local Unicast Addresses Link-Local Unicast Addresses Autoconfiguring IPv6 Addresses Demonstration: Configuring IPv6 Client Settings
Notes: Provide a brief overview of the lesson content.
20410D
8: Implementing IPv6

## Slide 12: IPv6 Address Structure
The number of network bits is defined by the prefix
Each host has 64-bits allocated to the interface identifier
Type of address | IPv4 address | IPv6 address
Unspecified | 0.0.0.0 | ::
Loopback | 127.0.0.1 | ::1
Autoconfigured | 169.254.0.0/16 | FE80::/64
Broadcast | 255.255.255.255 | Uses multicasts instead
Multicast | 224.0.0.0/4 | FF00::/8
Notes: In the previous lesson, you described to students what an IPv6 address looks like. In this topic, you need to describe how they can identify the network portion of an IPv6 address. Unlike IPv4, an IPv6 unicast address that is assigned to a host always uses a prefix of /64.
Take a few moments to describe the IPv6 equivalents to IPv4 special address.
20410D
8: Implementing IPv6

## Slide 13: Global Unicast Addresses
Global Routing
Prefix
001
Subnet
ID
Interface ID
48 bits
45 bits
64 bits
16 bits
Prefix Managed by IANA
Client Interface ID
Prefix Assigned to Top-level ISPs
Subnet Bits for Organizations
Are routable on the Ipv6 Internet
Allocate 16 bits for internal subnetting
Begin with 2 or 3 (2000::/3)
Notes: The key message for students to take away from this slide is that global unicast addresses are the equivalent of public IP addresses on the IPv4 Internet. Describe how an organization is provided with 16 bits for subnetting.
20410D
8: Implementing IPv6

## Slide 14: Unique Local Unicast Addresses
11111110
Subnet ID
Interface ID
Organization ID
FD00::/8
40
bits
16
bits
64
bits
8
bits
Are equivalent to IPv4 private addresses
Require the organization ID to be randomly generated
Allocates 16 bits for internal subnetting
Notes: The key information for students to understand about unique local addresses is that they are equivalent to IPv4 private addresses, because they are not routable on the Internet. It also is critical for students to understand that randomly generating the organization ID allows easier mergers between organizations.
20410D
8: Implementing IPv6

## Slide 15: Link-Local Unicast Addresses
000 . . . 000
1111 1110 10
Interface ID
64 bits
54 bits
10 bits
FE80::/8
Are automatically generated on all IPv6 hosts
Are similar to IPv4 APIPA addresses
Are sometimes used in place of broadcast messages
Include a zone ID that identifies the interface
Examples: fe80::2b0:d0ff:fee9:4143%3
fe80::94bd:21cf:4080:e612%2
Notes: Regardless of whether hosts have been assigned other IPv6 addresses, all hosts automatically generate a link‑local IP address that is used only on locally attached subnets. Unlike Automatic Private IP Addressing (APIPA) addresses, they are not optional and do not indicate a problem.
20410D
8: Implementing IPv6

## Slide 16: Autoconfiguring IPv6 Addresses
If Managed or Other flag set, check DHCPv6
6
Add prefixes
5
Check the router for prefixes
4
Check for a router on the network
3
Check for address conflicts by using neighbor solicitation
2
Derive a link-local address
1
IPv6 DHCP Server
6
IPv6 Router
5
4
3
IPv6 Client
2
1
Address autoconfiguration for IPv6 is a six-step process:
Notes: Be sure that students understand that a router can assign network prefixes to a client automatically, but a Dynamic Host Configuration Protocol (DHCP) server is required to assign other configuration options dynamically, such as a Domain Name System (DNS) server.
This slide is a summary of the six-step process used for IPv6 autoconfiguration. The steps are:
The client derives a link-local address. The client checks for address conflicts by using neighbor solicitation, and verifies that the link-local address is unique.
The client checks for routers on the network.
The client checks to see which prefixes are configured on the router.
The client adds the prefixes locally.
If the Managed or Other flag is set, the client checks for DHCPv6 to obtain other configuration information.
The next slide is a six-frame build slide that provides a step-by-step illustration of this example.
20410D
8: Implementing IPv6

## Slide 17: Autoconfiguring IPv6 Addresses
DHCPv6 information received
If Managed or Other flag set, check DHCPv6
6
Additional router prefixes
Add prefixes
5
Check the router for prefixes
4
Router configuration search
Check for a router on the network
3
Check for address conflicts by using neighbor solicitation
2
fe80::d593:e1e:e612:53e4%10
Derive a link-local address
1
IPv6 Client
IPv6 DHCP Server
IPv6 Router
6
5
4
3
2
1
The six-step process:
Notes: This is a 6-frame build slide.
It illustrates a simple example in which the network prefixes are obtained from the router, but additional configuration information is obtained from DHCP. Here is a breakdown of the six frames:
On the 1st of 6 frames:
There is an IPv6 client, an IPv6 router, and a IPv6 DHCP server.
The client derives the link-local address fe80::d593:e1e:e612:53e4%10.
On the 2nd of 6 frames:
The client checks for address conflicts by using neighbor solicitation, and verifies that the link-local address is unique.
On the 3rd of 6 frames:
The client checks for routers on the network.
On the 4th of 6 frames:
The client checks to see which prefixes are configured on the router. This is successful.
On the 5th of 6 frames:
The client adds the prefixes locally.
On the 6th of 6 frames:
If the Managed or Other flag is set, the client checks the DHCPv6 Server to obtain other configuration information.
8: Implementing IPv6
20410D

## Slide 18: Autoconfiguring IPv6 Addresses
Valid Lifetime
Preferred Lifetime
Time
Invalid
Tentative
Deprecated
Preferred
Valid
Autoconfigured IP Timeline
Notes: Use this line diagram to explain to students the states that a host's IPv6 address goes through during its lifecycle.
20410D
8: Implementing IPv6

## Slide 19: Demonstration: Configuring IPv6 Client Settings
In this demonstration, you will see how to:
  View IPv6 configuration by using ipconfig and Get-NetIPAddress
  Configure IPv6 on a domain controller and a server
  Verify IPv6 communication is functional
Notes: Preparation Steps
Start the 20410D‑LON‑DC1 and 20410D‑LON‑SVR1 virtual machines.
Demonstration Steps
View IPv6 configuration by using ipconfig and Get‑NetIPAddress
Sign in to LON‑DC1 and LON‑SVR1 as Adatum\Administrator with the password Pa$$w0rd.
On LON‑DC1, on the taskbar, click the Windows PowerShell® icon.
At the Windows PowerShell prompt, type ipconfig, and then press Enter.
Notice that this returns a link‑local IPv6 address.
At the Windows PowerShell prompt, type Get‑NetIPAddress, and then press Enter.
Notice that the Get‑NetIPAddress command returns a link‑local IPv6 address.
Configure IPv6 on LON‑DC1
On LON‑DC1, in Server Manager, click Local Server.
In the local server's Properties pane, next to Ethernet, click 172.16.0.10, IPv6 enabled.
In the Network Connections dialog box, right‑click Ethernet, and then click Properties.
Click Internet Protocol Version 6 (TCP/IPv6), and then click Properties.
In the Internet Protocol Version 6 (TCP/IPv6) Properties dialog box, click Use the following IPv6 address.
In the IPv6 address box, type FD00:AAAA:BBBB:CCCC::A.
In the Subnet prefix length box, type 64.
In the Preferred DNS server box, type ::1, and then click OK.
In the Ethernet Properties dialog box, click Close.
Close the Network Connections dialog box.
20410D
8: Implementing IPv6
(More notes on the next slide)

## Slide 20
Notes: Configure IPv6 on LON‑SVR1
On LON‑SVR1, in Server Manager, click Local Server.
In the local server's Properties pane, next to Ethernet, click 172.16.0.11, IPv6 enabled.
In the Network Connections dialog box, right‑click Ethernet, and then click Properties.
In the Ethernet Properties dialog box, click Internet Protocol Version 6 (TCP/IPv6), and then click Properties.
In the Internet Protocol Version 6 (TCP/IPv6) Properties dialog box, click Use the following IPv6 address.
In the IPv6 address box, type FD00:AAAA:BBBB:CCCC::15.
In the Subnet prefix length box, type 64.
In the Preferred DNS server box, type FD00:AAAA:BBBB:CCCC::A, and then click OK.
In the Ethernet Properties dialog box, click Close.
Close the Network Connections dialog box.
Verify that IPv6 communication is functional
On LON‑SVR1, on the taskbar, click the Windows PowerShell icon.
At the Windows PowerShell prompt, type ipconfig, and then press Enter.
Notice that both the link‑local IPv6 address and the IPv6 address that you have configured are displayed.
At a command prompt, type ping ‑6 lon‑dc1, and then press Enter.
Verify that you receive four replies from LON‑DC1 IPv6 address.
Type ping ‑4 lon‑dc1, and then press Enter.
Verify that you receive four replies from LON‑DC1 IPv4 address.
Type Test-NetConnection FD00:AAAA:BBBB:CCCC::A, and then press Enter.
Verify that you receive Ping Succeeded: True from LON‑DC1 IPv6 address.
Leave the virtual machines running after you complete the demonstration.
20410D
8: Implementing IPv6

## Slide 21: Lesson 3: Coexistence with IPv4
What Are Node Types? IPv4 and IPv6 Coexistence Demonstration: Configuring DNS to Support IPv6 What Is IPv6 over IPv4 Tunneling?
Notes: Briefly describe the lesson content.
20410D
8: Implementing IPv6

## Slide 22: What Are Node Types?
IPv4 Network
IPv6 Network
IPv4/IPv6 Node
IPv4-only Node
IPv6-only Node
Notes: It is important that students understand how to classify nodes. When planning an IPv6 network, they must know the state of the network’s nodes or hosts. Explain to students that by describing the nodes with the proper terminology, they can define the nodes' abilities on the network. This also is important for tunneling, because there are certain kinds of tunnels that require specific types of nodes.
20410D
8: Implementing IPv6

## Slide 23: IPv4 and IPv6 Coexistence
Windows Server 2012 uses a dual IP layer architecture that supports IPv4 and IPv6 in a single protocol stack
DNS records required for coexistence are:
Host (A) resource records for IPv4 nodes
IPv6 host (AAAA) resource records
Reverse lookup pointer (PTR) resource records for IPv4 and IPv6 nodes
Notes: The most important point that students need to learn in this topic is that IPv4 and IPv6 can coexist. Students also should be aware that IPv6 requires additional DNS records.
20410D
8: Implementing IPv6

## Slide 24: Demonstration: Configuring DNS to Support IPv6
In this demonstration, you will see how to:
  Configure an IPv6 host (AAAA) resource record for an IPv6 address
  Verify name resolution for an IPv6 host (AAAA) resource record
Notes: Preparation Steps
You must have completed the previous demonstration in this module before you begin this demonstration. You need the 20410D‑LON‑DC1 and 20410D‑LON‑SVR1 virtual machines to complete this demonstration. They should be running after the previous demonstration.
Demonstration Steps
Configure an IPv6 host (AAAA) resource record
On LON‑DC1, in Server Manager, click Tools, and then click DNS.
In DNS Manager, expand LON‑DC1, expand Forward Lookup Zones, and then click Adatum.com.
Read the records listed for the zone, and notice that LON‑DC1 and LON‑SVR1 have registered their IPv6 addresses dynamically with the DNS server.
Right‑click Adatum.com, and then click New Host (A or AAAA).
In the New Host window, in the Name box, type WebApp.
In the IP address box, type FD00:AAAA:BBBB:CCCC::A, and then click Add Host.
Click OK to clear the success message.
Click Done to close the New Host window.
Verify name resolution for an IPv6 host (AAAA) resource record
On LON‑SVR1, if necessary, open a Windows PowerShell prompt.
At the Windows PowerShell prompt, type ping WebApp.adatum.com, and then press Enter.
Verify that you receive four replies from WebApp.adatum.com IPv6 address.
Type Test-NetConnection WebApp.Adatum.com, and then press Enter.
Verify that you receive Ping Succeeded: True from WebApp.Adatum.com IPv6 address.
After you complete the demonstration, revert all virtual machines.
20410D
8: Implementing IPv6

## Slide 25: What Is IPv6 over IPv4 Tunneling?
Upper Layer Protocol Data Unit
Extension Headers
IPv6
Header
IPv4 Header
Upper Layer Protocol Data Unit
Extension Headers
IPv6
Header
IPv4 Packet
IPv6 Packet
IPv4
IPv6
IPv4 Packet
IPv6 Packet
IPv6 over IPv4 tunneling allows IPv6 to communicate through an IPv4 network
Notes: The concept of tunneling one protocol inside another might not be familiar to some students. Provide other examples of tunneling to clarify, such as:
Remote Procedure Call (RPC) over HTTP for Outlook® Anywhere
Virtual Private Network (VPN) connections
20410D
8: Implementing IPv6

## Slide 26: Lesson 4: IPv6 Transition Technologies
What Is ISATAP? What Is 6to4? What Is Teredo? What Is PortProxy? Process for Transitioning to IPv6
Notes: Provide a brief overview of the lesson content.
20410D
8: Implementing IPv6

## Slide 27: What Is ISATAP?
IPv6-Capable Network
ISATAP Host
ISATAP Host
ISATAP Router
IPv4-only Intranet
Allows IPv6 communication over an IPv4 intranet
Can be enabled by configuring an ISATAP host record
Connects all nodes to a single IPv6 network
Uses the IPv4 address as part of the IPv6 address
    Private address: FD00::0:5EFE:192.168.137.133
    Public address: 2001:db8::200:5EFE:131.107.137.133
Notes: Ensure that students understand that ISATAP is suitable only within a private network, and that they cannot use it over the Internet. In the lab, students will configure an ISATAP router to enable communication between an IPv4‑only subnet and an IPv6‑only subnet. Therefore, you must ensure that students understand the purpose of the ISATAP router and the host record.
20410D
8: Implementing IPv6

## Slide 28: What Is 6to4?
Provides IPv6 connectivity over the IPv4 Internet
Works between sites or from host to site
Is not suitable for scenarios using NAT
Uses the following network address format:
  2002:WWXX:YYZZ:Subnet_ID::/64
To enable Windows Server 2012 as a 6to4 router:
Enable ICS
Use Windows PowerShell
6to4 Router
IPv6/IPv4
6to4 Router
IPv6/IPv4
IPv6/IPv4
IPv6/IPv4
IPv4 Internet
Notes: Stress that the purpose of 6to4 is for IPv6 connectivity over the IPv4 Internet, rather than an internal network. Also, remind students that 6to4 is not suitable for Network Address Translation (NAT). In most cases, they will enable 6to4 on existing network infrastructure components rather than using Windows Server 2012 as a router.
20410D
8: Implementing IPv6

## Slide 29: What Is Teredo?
Teredo Client
NAT
NAT
Teredo Server
IPv4 Internet
Teredo:
Enables IPv6 connectivity over the IPv4 Internet through NAT
Requires a Teredo server to initiate communication
Can be configured with the cmdlet Set-NetTeredoConfiguration
Windows Server 2012:
Can be configured as a client, server, or relay
Is configured as a client by default
Must be an enterprise client on domain networks
Notes: Because Teredo and 6to4 perform a similar function it is essential that students understand the difference between the two. The main benefits of Teredo are its ability to traverse NAT, and the availability of public Teredo servers.
20410D
8: Implementing IPv6

## Slide 30: What Is PortProxy?
Use PortProxy to:
Provide IPv6-only hosts with access to IPv4-only applications
Provide access between IPv4-only and IPv6-only hosts
Limitations of PortProxy:
Only TCP applications
Cannot change embedded address information
Notes: PortProxy has some limitations that you should mention to students, including that:
PortProxy can proxy only TCP data.
PortProxy can support only application-layer protocols that do not embed addresses or port information inside the application-layer data. PortProxy cannot change address information at the application level.
Additional Reading: For more information about IPv6 Transition Technologies, refer to "IPv6 Transition Technologies" at http://go.Microsoft.com/fwlink/?LinkID=112079&clcid=0x409.
20410D
8: Implementing IPv6

## Slide 31: Process for Transitioning to IPv6
To transition from IPv4 to IPv6 you must:
Update applications to support IPv6
Update routing infrastructure to support IPv6
Update devices to support IPv6
Update DNS with records for IPv6
Upgrade hosts to IPv4/IPv6 nodes
Notes: Stress to students that most organizations add IPv6 to a functional IPv4 environment, and remove IPv4 only when they no longer need it. Organizations most likely will continue to use IPv4 internally for an extended time.
20410D
8: Implementing IPv6

## Slide 32: Lab: Implementing IPv6
Exercise 1: Configuring an IPv6 Network Exercise 2: Configuring an ISATAP Router
Logon Information
Virtual machines 20410D‑LON‑DC1
20410D‑LON‑RTR
20410D‑LON‑SVR2
User name Adatum\Administrator
Password Pa$$w0rd
Estimated Time: 45 minutes
Notes: Before students begin the lab, read the lab scenario and display the next slide. Before each exercise, read the scenario associated with the exercise to the class. The scenarios give context to the lab and exercises, and help to facilitate the discussion at the end of the lab. Remind students to complete the discussion questions after the last lab exercise.
Exercise 1: Configuring an IPv6 Network
For the first step in configuring the test lab, you need to configure LON‑DC1 as an IPv4‑only node, and LON‑SVR2 as an IPv6‑only node. You also need to configure LON‑RTR to support IPv6 routing by adding a network to an interface on the IPv6 network, and by enabling router advertisements. The router advertisements allow the IPv6 clients on the IPv6 network to obtain the correct IPv6 network automatically through stateless configuration.
Exercise 2: Configuring an ISATAP Router
After configuring the infrastructure for an IPv4‑only network and an IPv6‑only network, you need to configure LON‑RTR as an ISATAP router to support communication between the IPv4‑only nodes and the IPv6‑only nodes.
To configure LON‑RTR as an ISATAP router, you need to enable the IPv4 interface as the ISATAP router. Then you configure an IPv6 network on the ISATAP interface and enable advertising of the network route that includes that network. ISATAP clients will obtain the IPv6 network automatically from the advertisements.
To enable ISATAP automatically on clients, you need to create an ISATAP host record in DNS. Clients that can resolve this name automatically become ISATAP clients. To allow clients to resolve this name, you must remove ISATAP from the global query block list on the DNS server.
20410D
8: Implementing IPv6

## Slide 33: Lab Scenario
The IT manager at A. Datum Corporation has been briefed by several program and application vendors about newly added support for IPv6 in their products. A. Datum Corporation does not have IPv6 support currently. However, the IT manager wants you to configure a test lab that uses IPv6. As part of the test lab configuration, you also need to configure ISATAP to allow communication between an IPv4 network and an IPv6 network.
Notes: 20410D
8: Implementing IPv6

## Slide 34: Lab Scenario
This is the layout of the completed test environment
Notes: 20410D
8: Implementing IPv6

## Slide 35: Lab Review
Did you configure IPv6 statically or dynamically in this lab? Why did you not need to configure LON-DC1 with the IPv4 address of the ISATAP router?
Notes: Lab Review Questions
Question
Did you configure IPv6 statically or dynamically in this lab?
Answer
You configured IPv6 dynamically in this lab. You added both IPv6 networks to the router, and router advertisements configured LON‑DC1 and LON‑SVR2 with the correct network address.
Question
Why did you not need to configure LON-DC1 with the IPv4 address of the ISATAP router?
Answer
The default configuration for Windows client operating systems is set to resolve ISATAP by using DNS to locate the IPv4 address of the ISATAP router. LON‑DC1 used the default configuration.
20410D
8: Implementing IPv6

## Slide 36: Module Review and Takeaways
Review Questions Best Practices
Notes: Module Review Questions
Point students to the appropriate section in the course so that they are able to answer the questions that this section presents.
Question
What is the main difference between 6to4 and Teredo?
Answer
Both protocols allow IPv6 connectivity over the IPv4 Internet. However, only Teredo is able to provide connectivity through NAT.
Question
How can you provide a DNS server to an IPv6 host dynamically?
Answer
To provide a DNS server to an IPv6 host dynamically, you must use DHCPv6. You can use router advertisements to provide the network portion of an IPv6 address, but router advertisements cannot distribute DNS server IP addresses.
Question
Your organization is planning to implement IPv6 internally. After some research, you have identified unique local IPv6 addresses as the correct type of IPv6 addresses to use for private networking. To use unique local IPv6 addresses, you must select a 40‑bit identifier that is part of the network. A colleague suggests using all zeros for the 40 bits. Why is this not a good idea?
Answer
The 40‑bit organization identifier in a unique local IPv6 address should be generated randomly. This makes it as likely as possible that no two organizations will use the same organization identifier. If two organizations use the same organization identifier, then the networks cannot be joined together after a merger.
20410D
8: Implementing IPv6
(More notes on the next slide)

## Slide 37
Notes: Question
How many IPv6 addresses should be configured on an IPv6 node?
Answer
There is no specific number of IPv6 addresses that an IPv6 node should have. It depends on the organization’s configuration. Each IPv6 node has a link‑local IPv6 address. Additionally, it also may have a unique local IPv6 address for internal connectivity and a global unicast IPv6 address for IPv6 Internet connectivity.
Best Practices
Use the following best practices when implementing IPv6:
Do not disable IPv6 on Windows 8 or Windows Server 2012.
Enable coexistence of IPv4 and IPv6 in your organization rather than using transition technologies.
Use unique local IPv6 addresses on your internal network.
Use Teredo to implement IPv6 connectivity over the IPv4 Internet.
20410D
8: Implementing IPv6